## Slide 1
Real Camera Real-time Rendering of Physically Based Optical Effects in Theory and Practice Yoshiharu Gotanda tri-Ace, Inc.

## Slide 2: Camera
A camera is made from a lot of components
  This course deals with components that make visual differences

## Slide 3: Camera Components
Body
  Shutter
  Sensor
Lens
  Optical lenses
  Aperture
  Barrel

## Slide 4: Exposure
Proper exposure
  When you take an image with a camera
    Proper exposure (brightness) is required
      Need to control multiple factors
        Time value (shutter speed)
        F-number (aperture)
        Film speed (sensor sensitivity)

## Slide 5: Exposure Value and APEX
A value for ‘exposure’
  To combine ‘time value’ and ‘F-number’
: F-number
: Exposure time (shutter speed)
: Average scene luminance (brightness)
ISO arithmetic film speed
: Reflected-light meter calibration constant
Constant that establishes the relationship between and
=

## Slide 6: Shutter
A device that allows light to pass for a determined period of time (exposure time)
  Mechanical or electrical
  Controls exposure (brightness of an image)
  Longer exposure time produces longer motion blur

## Slide 7: Sensor
To receive photons and convert into electrical signals
  Photographic film was used in the past
  Higher (ISO) sensitivity yields more noise
    Exposure setting affects the amount of noise

## Slide 8: Noise vs. Sensitivity
ISO100
400
1,600
6,400
12,800
25,600
51,200
102,400

## Slide 9: Camera Lens
The main part of this course
  A camera lens has:
    Multiple optical lenses
    An aperture
    A barrel
    Motors

## Slide 10: Optical Lens
Transmissive optical device that affects the focus of a light beam through refraction
  Lens is necessary to collect light to acquire an image with the required exposure

## Slide 11: Camera Lens Requirements
A camera lens needs
  Variable focus distance from close to infinite
  Fast exposure (small F-number)
  Zoom (optional)
  Image stabilization (optional)

## Slide 12: Camera Lens Requirements
Multiple optical lenses are necessary to satisfy the requirements
  Multiple lenses cause optical side effects
    Distortion
    Aberrations
  More lenses are required to remove side effects
    Not perfect with a reasonable number of lenses

## Slide 13: Optical Effects
Physical and optical limitations yield various optical effects
  Bokeh
  Aberration
  Glare (diffraction)
  Vignetting
  Anamorphic lens effects
  Distortion
  Ghost

## Slide 14: Bokeh
Produced by optical lenses and an aperture
  The aperture mechanism produces different shapes of bokeh
  Multiple lenses yield various aberrations which produce different appearances of bokeh

## Slide 15: Iris Diaphragm
Camera has an iris diaphragm for an aperture
  It typically has multiple blades to control exposure
  Curved blades are often used (circular aperture)
    Cheaper systems use straight blades or fixed diaphragm
    Curved blades yield more complex optical behavior

## Slide 16: Circular Aperture
The shape of aperture is…
  More circular when opened
  Tends towards a polygonal shape as it is closed
f/5.6
f/8.0
f/13
Fully opened

## Slide 17: Glare Shape
Glare effect varies by the number of blades
Even numbers of blades produce the same number of spikes (8 blades)
  Odd numbers of blades produce twice the number of spikes (9 blades)

## Slide 18: Glare Shape
Circular aperture produces more complex glare effects

## Slide 19: Glare Shape and F-number
f/2.8
f/3.2
f/3.5
f/4.0
f/5.6
f/8.0
f/11
f/16
f/22
Shorter and thinner
Longer and thicker

## Slide 20: Depth of Field
F-number also controls depth of field
  The nearest and farthest objects in a scene that appear acceptably sharp in an image

## Slide 21: Depth of Field and F-number
f/2.8
f/4.0
f/5.6
f/8.0
f/11
f/16
f/22
f/32

## Slide 22: Focus and View Angle
Changing focus distance optically causes view angle (focal length) variations (focus breathing)
  The theoretical reason will be explained later
Focus on this glass
Easily recognizable view angle difference
This lens can focus between 1.5m and Inf. Even with a 30cm focus distance change as shown in these pictures, recognizable view angle change appears.

## Slide 23: Focus Breathing
When focusing on a closer point, field of view gets narrower

## Slide 24: Focus Breathing

## Slide 25: Aberrations
Multiple optical lenses yield a variety of different aberrations
  Spherical Aberration
  Coma
  Field Curvature
  Oblique Astigmatism
  Distortion

## Slide 26: Aberrations
Different configurations of multiple lenses produce a variety of bokehs
Pictures from [Kawase 2012]

## Slide 27: Optical Vignetting
Phenomenon that light entering near the edge of the lens at an obtuse angle can’t reach the sensor
  Because it is obstructed by the lens barrel
  The actual physical phenomenon is very complicated
Blue line indicates that ray is obstructed
Sensor

## Slide 28: Optical Vignetting
Recognized as…
  The corners of the picture are darkened
  “Cat eye effect” (eclipsed bokeh)
24mm F2.8
24mm F5.6

## Slide 29: Anamorphic Lens
Legacy lenses that are designed for film
  To make full use of the available film, a lens is used during photography to stretch the image vertically
  Effects caused by the lens make the picture “retro.”
    Recently, some (Sci-fi) films or games use anamorphic lens effects to make them “retro”-style

## Slide 30: Anamorphic Lens Effects
Panasonic LA7200 Anamorphic Lens Flare by Andrei Jikh
http://vimeo.com/9493224#at=0

## Slide 31: Lens Ghosts
Undesired artifacts caused by multiple reflections and refractions in a camera lens
  Various shapes of ghosts are observed
    Lens opening
    Aperture
    Vignetting

## Slide 32: Lens Ghosts
Emphasized

## Slide 33: Effects by Camera Mechanism
 | Exposure | Depth of Field | Bokeh Shape | View Angle | Motion Blur | Noise | Vignetting | Ghosts
Shutter | x |  |  |  | x |  |  | 
Sensitivity | x |  |  |  |  | x |  | 
Zoom | (x) | x | (x) | x |  |  | x | x
Focus | x | x | (x) | x |  |  | x | x
Aperture | x | x | x |  |  |  | x | x

## Slide 34: Conclusion
A camera has multiple factors to take an intentional image
  Changing a factor to control a parameter always has side effects

## Slide 35: Acknowledgements
Masaki Kawase
Masanori Kakimoto
Kristian Spoerer